## Slide 1: ELEMENTS OF ENGINEERING ME144
Prof. Bhargav Shobhana
Department of Civil Engineering
bhargavshobhana.cv@charusat.ac.in

## Slide 2: Syllabus
11. | Introduction to Surveying
11.1 | Definition of surveying
11.2 | Objects of surveying, Uses of surveying
11.3 | Primary divisions of surveying, Principles of surveying
11.4 | List of classification of surveying, Definition: Plan and Map, Scales : Plain scale and Diagonal scale, Conventional Symbols
11.5 | Introduction to linear and angular measurements, Concepts of land profiling

## Slide 3: Surveying and levelling
Surveying: Is the art of determining the relative position of various points above, on or below the surface of the earth.
Levelling: Is the art of determining the relative vertical distance of different points
  Measurement Taken
    Vertical distance
    Horizontal Distance
    Angle
      Horizontal
      Vertical
  Computation
  Preparation of maps and plans
  Used for
    Calculation of length
    Area
    Volume
Art of tracing the points on a map to the ground
Purpose of the surveying:
  Take measurements to determine the relative position of the point
  Make layouts , maps or plans to mark the proposed position of structure on the surface
  Determine the area, volume and other relative quantity.

## Slide 4: Use of Surveying
Preparation of Map
  To prepare the topographical maps
  Prepare cadastral maps showing boundaries, houses and properties
  Engineering map
  Military map
  Geological map
  Archaeological map

## Slide 5: Primary Divisions of Surveying
Primary Classification:
  Division is based on the basis weather the curvature of the earth is taken in to consideration or not
    Plane Surveying :
      Curvature of earth is neglected and assumed as plane surface
      Horizontal surface:
      Vertical line:
      Plane survey can be used when considered for a small area (Less than 250 Km2)
      Degree of accuracy is comparatively low
    Geodetic surveying
      Curvature of earth is taken in to consideration
      Large distance and large area
      Refined methods of observation and adjustment

## Slide 6: Difference between plane survey and geodetic survey
Plane Survey
  Curve of the earth is ignored
  Used for relatively small area (<250 SqKm)
  Used for establishing relatively less important area
  Direction of plumb lines are assumed to be parallel to one another
  Lower accuracy
  Angle of triangle formed by any three line considered to be plane
Geodetic Survey
  Curvature of earth is taken it to consideration
  Used for larger area (>250SqKm)
  Used for establishing precise points
  Direction of plumb lines are different at various points
  High accuracy and high precise instruments are used
  Angle of triangle formed by any three line considered to be plane

## Slide 7: Principles of Surveying:
  Work should be done from “whole to part” and not from “part to whole”
  Position of new station should be fixed by at least two independent methods
P
Q
R
P
Q
R
P
Q
R
P
Q
R
P
Q
R
P
Q
R

## Slide 8
8
Classification of Survey
Surveying
Instrument used
Nature of the field
Method Used
Object of Survey
A

## Slide 9
Hydrographic Survey:
  On or near the body of water.
  Locating shore line
  Estimation of water flow
  Profiling of area beneath the water
Land Survey
  Determining boundaries and area of land
    Topographic survey:
    City survey:
    Engineering survey: design and planning of engineering work
      Reconnaissance survey
      Preliminary survey
      Location Survey
    Cadastral Survey: Boundaries of private bodies
Astronomical survey:
  Determination of earth location (lat, long, time by observing astronomic bodies
Aerial Survey
  Conducted from aircraft
  Photographs were taken and study
Cadastral
Hydrographic
Topographic
Land
City
Engineering
Nature of the field
B
Classification Nature of the field
Aerial Survey
Astronomical

## Slide 10: Classification based on objective of survey
Objective
Control Survey
Military survey
Archaeological survey
Mine survey
Geological Survey
C
Classification based on Method used
Method
Triangular Survey
Travers survey
D
Classification based on instrument used
Instrument
Chain
Theodolite
Compass
Tacheometric survey
Plane table Survey
E
Photometric Survey

## Slide 11: Plans and Maps
Plan
Plans are a set of two-dimensional diagrams or drawings used to describe a place or object, or to communicate building or fabrication instructions
Plans are usually scale drawings, meaning that the plans are drawn at specific ratio relative to the actual size of the place or object.
Plans are large scale (1:10, 1: 20 etc)
Map
A map is a visual representation of an area—a symbolic depiction highlighting relationships between elements of that space such as objects, regions, and themes
Many but not all maps are drawn to a scale, allowing the reader to infer the actual sizes of, and distances between, depicted objects
Maps are small scale (1:1000, 1:5000 etc)

## Slide 12: Conventional symbols

## Slide 13: Conventional symbols

## Slide 14: Scale
Scale: Is the ratio of distance on the paper (Plan or map) to the distance on the ground
Scale=
Selection of scale depends on
  Purpose
  Size
  Required precision
Classification
  Large scale: 1cm =10 m or less than 10m
  Medium scale: 1cm = 10 m to 100 m
  Small : 1 cm = 100m or more than 100m
Type of scale
  Engineers scale:
    Indicated by a statement (1 cm= 5 m)
  Representative fraction:
    Indicated by a ratio of the distance on the plan to the corresponding distance on the ground ( scale of 1cm=5m in RF is
    RF is unit less
  Graphical scale:
  Chord scale:
  Comparative scale

## Slide 15: Scale
Graphical scale:
  Scale which is drawn on the plan itself
    Types:
      Plain scale: Possible to measure units and its submultiple.
      Diagonal Scale: Possible to measure unit, submultiple and further submultiple
    Importance
      Avoid the change in scale because of shrinkage of paper
      Shrunk scale= Shrinkage factor x Original scale
      Shrinkage factor =
      Shrinkage factor will always less than 1
      Corrected distance=
      Corrected area =
10
20
30
10 8 6 4 2 0
34
Plain scale
Diagonal scale
  Comparative scale:
    Designed to read two units of measures which are interconnected.
    Representative fractions for both measures are same and can easily computed
  Chord scale:
    Is used to measure angles or set off angles with considerable accuracy

## Slide 16: Examples
If scale is 1 cm = 10 m , RF is ???
= or 1 :1000
If scale is 1 cm = 100 m , RF is ???
= or 1 :10000

## Slide 17: Example
A 10 km long road is indicated in a map by 10cm straight line. Calculate the scale and RF
10 cm on drawing sheet = 10 km on ground
RF = = or 1 : 100000

## Slide 18: Example
An area of 49 cm2 of a map represents an area of 2401 km2. Find the scale and R.F. of Map?
ie. 49 cm2 = 2401 km2
Or 1 cm = = 7 km
scale 1 cm = 7 km
RF = =

## Slide 19: Example
Construct a plain scale of RF 1/500 to measure up to meters and represent 37 m on the scale.
Construct a diagonal scale of RF 1/500 to measure up to meters and represent 37.5 m on the scale.
0
10
20
30
10
37
0
10
20
30
10
37
38
37.5